## Slide 1: DESIGN OF AN INDOOR AUTONOMOUS MOBILE ROBOT BASED ON ROS
Speaker: Hoàng Văn Tiến

## Slide 2: Content
System Design Process
Technical Requirements Definition
Hardware System Design
Software System Design
System Testing

## Slide 3: System Design Process

## Slide 4: Technical Requirements Definition
Functional requirements
  Self-localization
  Mapping
  Navigation
  Obstacle avoidance
Technical specifications
  Mass
  Dimensions
  Loads
  Velocities

## Slide 5: Hardware System Design
Design of system structure
  Based on technical requirements

## Slide 6: Hardware System Design
Design and selection of hardware modules

## Slide 7: Hardware System Design
Making a hardware prototype
  Manufacturing mechanical details
  Assemble mechanical details
  Integrating sensors, actuators and the hardware of embedded system into mechanical system
  Take mechanical tests

## Slide 8: Software System Design
Design of software architecture

## Slide 9: Software System Design
Design of software architecture
  Package “robot_description ”: provide the robot model
  Package “robot_control”: provide the base controller
  Packages for getting data from sensors: encoder, laser, IMU
  Package “robot_localization”:fuses data from IMU, encoder and creates resulted odometry
  Navigation packages for self-localization, mapping, motion planning

## Slide 10: Software System Design
Create the “robot_description”

## Slide 11: Software System Design
Create packages for sensors and actuators
  Find suitable packages for the given sensors
  http://wiki.ros.org/Sensors
  Create the package for controlling base motion
  Create the package for wheel odometry

## Slide 12: Software System Design
Create packages for robot navigation
  Install the Navigation Stack
Packages for global planner:
global_planner
Navfn
carrot_planner
Packages for local planner:
base_local_planner
dwa_local_planner
eband_local_planner
teb_local_planner
mpc_local_planner

## Slide 13: Software System Design
Create packages for robot navigation
  Configure the Navigation Stack
    Costmap Configuration (local_costmap) & (global_costmap)
    Global Planner Configuration
    Local Planner Configuration
    AMCL Configuration (Adaptive Monte Carlo Localization (AMCL))
  Creating a Launch File for the Navigation Stack
    For running AMCL
    For mapping
    For motion planning
  Running the Navigation Stack

## Slide 14: System Testing
Functional testing
  Self-localization
  Mapping
  Motion planning
  Obstacle avoidance
Specification tests
  Loading
  Max speed
  Run time